## Slide 1: Mcsim Python toolbox
How to structure it?
Mathias Marley, Feb 2022

## Slide 2: Goals
Main goal: a tool that is actually used and developed
Ease of use
Ease of development
«Sufficient» documentation
Flexible and easy to modify for users

## Slide 3: Main structure
Library of functions
Library of model data
User scripts (load model data and run simulations)
Model-generating scripts

## Slide 4: Models
A «model» consists of
  A model function, located in function library
  A model parameter file, stored in .pkl files

## Slide 5: Main libraries of function
MClib: general functions
MCmod: model functions
MCcon (control), MCenv (environmental), Mcsens (sensors)???

## Slide 6: Model functions
The «core» of MCsim Python
Performs single time step integration of dynamic models
Arguments:
  state, control input and disturbance input at current time step
  Model parameters
Output:
  state at next time step

## Slide 7: Model parameters
Model parameters are given by dictionary objects
  parV: vessel parameters
  parA: actuator parameters
Stored to file using pickle
  parV_RVG3DOF.pkl contains vessel data for RVG 3DOF model
  parA_RVG.pkl contains actuator data for RVG
«Verified» model parameters are uploaded to github
Additionally example scripts to generate parV, parA etc are uploaded.

## Slide 8: Using the toolbox
The main «user interface» is scripts that
  Load model data from file
  Initialize and run simulations by calling model functions in a for-loop